## Slide 1: GPIODVS General Purpose Intra-Operation Dynamic Voltage Scaling
Daniel Moore
November 3rd, 2016

## Slide 2: Agenda
Problem Definition + Abstract
PEGMA + IODVS
PRIME
  STM32F429 Discovery Board
  ADSM300-F
  PPS-330D
  DEB429A
PACER
Conclusions + Future Work

## Slide 3: Motivating Example: Logging Sensor
Upon detecting a loss of power
MCU goes into sleep mode
Wakes up periodically
Samples external temperature sensors
Logs them to EEPROM
EEPROM dominates energy consumption
Decreases logging lifespan
Communicates via RS485
CAT5 Resistance: 29Ω / 1000ft
; Need 6V at load
Assume 4 devices @ 25mA
Assume 12Vdc output
Ω
RS485 is rated for 4000ft over CAT5
Distance limited by power consumption, not line impedance
50mA per device is worst-case
  Can we decrease the worst case and thereby increase battery life, increase maximum distance and potentially decrease cost?
Commercial / Industrial Temperature Logger
    Power Supply
    RS485 Communications
    Non-Volatile Storage (EEPROM)
    Micro-controller
    Analog Input

## Slide 4: Motivating Example: Electricity Meter
Metrology MCU
Uses EEPROM
  Energy Usage
  Demand Intervals
  Profile Information
  NV-RAM
Communications MCU
Uses Serial flash
  Network routing data
  Firmware Updates
  NV-RAM
Capacitor allows the system to run for a period of time after power fails
Residential / Commercial Electricity Meter
  Power Supply / Metering
  Metering MCU
  Metering EEPROM
  Communications MCU
  Communications Serial Flash

## Slide 5
Some values need to be updated constantly and preserved across power failures
Typically indexes into logs
Energy accumulations
Status information
EEPROM has a limited write-cycle count (~1,000,000)
Serial flash is typically ~100,000
Solution: Use RAM, and interrupt to back it up as power fail occurs
Requires a capacitor capable of holding Vdd while backup is in progress
Actual communication is only 7.7% of the total write time. The other 92.3% is a mandatory wait period imposed by the chip ‘page-write time’
How can we decrease the energy consumed during the page write time?
Storage capacity is best described as energy limited!
NV-RAM Functionality
  Maximum Clock Frequency
  MCP25AA512 SPI EEPROM
  20 MHz (4.5 ≤ Vcc ≤ 5.5)
  10 MHz (2.5 ≤ Vcc ≤ 5.5)
  2 MHz (1.8 ≤ Vcc ≤ 5.5)
  Numonyx M25PX16
  75/33 MHz (2.7 ≤ Vcc ≤ 3.6)
  50/25 MHz (2.3 ≤ Vcc ≤ 2.7)
  Comms speed is voltage-dependent
  Write delays are voltage-independent

## Slide 6: Abstract
Peripheral devices in embedded systems are designed to include slack in both supply voltage and execution time.
GPIODVS exploits both types of slack in order to decrease both energy consumption and latency.

## Slide 7: Related Work / Objectives
Dynamic Voltage and Frequency Scaling (DVFS)
  and max frequency is determined by V
  Maximum performance (typically linearly) tracks applied voltage
  Common in microprocessors and gaining popularity in microcontrollers
Dynamic Power Management (DPM)
  where α corresponds to the ratio of active gates
  Sleep / Deep Power down modes
  Energy is saved while the device is not in use
  Results in increased response time (a wake up time)
    There is a lot of research dedicated to mitigating this (prediction / modelling)
Intra-Operation Dynamic Voltage Scaling (IODVS)
  Realize the power savings afforded by low performance states as the device is operating
  Response time is unaffected
Peripheral Activity Completion Recognition and Estimation (PACER)
  Identifies and minimizes peripheral operation time margin

## Slide 8: IODVS How: PEGMA
Peripheral Energy Generation Measurement and Allocation
4x + 1 input (boost) SMPS
3x output boost SMPS
8 independently adjustable buck SMPS domains
  MCU: STM32F205
    2x 10-bit DAC
    3x 12-bit ADC (2 MSPS per)
  Analog
  SRAM
  SPI Peripherals
    EEPROM
    Serial Flash
    Temp/Humidity Sensor
    Micro-SD Card
  Battery Charging
  Communications
    RS232
    RS485
    Bluetooth
    Zigbee
  LEDs / Pushbuttons
  Relays
I/O Voltage and Current Measurement on each SMPS
  Effectively sub-metering the board
  Allows us to measure efficiency

## Slide 9: Adjustable SMPS + Current Measurement
TPS62240 efficient at light loads
  ~80% at 1mA
I/O current measured by MAX4376
  “High Side” sense resistor is used, differential across is multiplied by the amplifier gain
  2MHz GBP, G = 20
Output Voltage modulated by current into the FB pin
  Therefore D9 allows the SMPS to enter a ‘default’ state
  And U25 / R105 allow FB current to be modulated by BUCKADJ3
  C144 holds the adjustment voltage so that other domains can be ‘refreshed’ in round robin fashion

## Slide 10: Peripheral Domain
Honeywell HIH6130 (I2C) Temperature/Humidity Sensor
  Vmax: 5.5V
  Vmin: 2.3V
Microchip 25AA512 EEPROM
  Vmax: 5.5V (20MHz)
  Vmin: 1.8V (2MHz)
Numonyx M25PX16 (16Mbit)
  Vmax: 3.6V (50MHz)
  Vmin: 2.3V (25MHz)
SPI Mode SD Cards
  Lexar SDSC: 1.0GB
  Sandisk: SDSC 1.0GB
  Swissbit: SDSC 512MB
  Kingston: SDSC 2.0GB
    Vmax: 3.6V
    Vmin: 2.7V (operating)
    Vmin: 2.0V (Idle/Read)

## Slide 11: Assumptions and Methods
Assumptions
  Measurements are for the set of peripherals (not individually metered)
  Only Datasheet specifications form the peripheral power profile
  Matched signaling voltages between MCU and peripheral
Test setup
  Tests use random data and addresses for memory devices
  Average 2048 test results
    Should be deterministic as possible
  Use as high a sampling frequency as the operation will allow
    Buffer size is 10240 samples * 4 channels including state
    Therefore a 10ms test can use about a 1us sample rate

## Slide 12: Peripheral Power Profiles
Each device driver contains a lookup table of state-voltage pairs
As the device enters a new state, the voltage is changed to correspond with the requirements of that state
Setup the onboard peripheral to correspond with the ability of the device
  This was generally abandoned because it was found that the MCU could end up charging the domain via the communicating port pins
  But it does apply to I2C devices

## Slide 13: Microchip 25AA512 EEPROM
128bytes written and verified at 7.5MHz
Voltage spike @ 1ms hits approximately 20mA, is measured and integrated
State | Static (uJ) | IODVS (uJ) | Delta
Idle | 10.24 | 3.49 | -65.91%
Write | 13.79 | 17.85 | 29.47%
Wait | 64.59 | 33.71 | -47.80%
Verify | 17.58 | 17.40 | -1.02%
Idle | 8.81 | 7.96 | -9.57%
Total | 115.02 | 80.43 | -30.07%

## Slide 14: Numonyx 25PX16 Serial Flash
Read 4K subsector, modify 128B within the (cached) subsector
Rewrite the subsector 1 page (256B) at a time
Read the 4K subsector, verify against the cached copy
*Accumulated Write and Wait States
State | Static (uJ) | IODVS (uJ) | Delta
Idle | 10.73 | 5.63 | -47.58%
Read | 71.51 | 72.36 | 1.19%
Erase | 2.47 | 2.47 | -0.13%
Write* | 89.48 | 99.16 | 10.82%
Wait* | 574.84 | 365.75 | -36.37%
Verify | 83.78 | 52.77 | -37.02%
Idle | 38.92 | 38.20 | -1.85%
Total | 2666.18 | 1614.57 | -39.44%

## Slide 15: Micro-SD Card (SPI Mode) Write Operation
Protocol is polling based, making it difficult to conform to our assumption that all communication take place at the same voltage … but not impossible
Power Up
(1ms < t < 35ms)
Initialize
(10ms < t < 1000ms)
Poll
(0 < t < 250ms)
Idle
Write Command
(~1ms)
Enter / Exit Power Down*
Read (Verify)
(~1ms)

## Slide 16: SD-Card Timing Variations
These tests tend to be non-deterministic because of the SD-Card protocol and onboard MMU.
Some operations complete near the 160ms mark, some near the 180ms mark.
Optimizing the wake-up-and-poll time is under further research

## Slide 17
Sandisk Micro-SD Card
Lexar Micro-SD Card
Energy Usage | Static (uJ) | IODVS (uJ) | Delta
Idle | 124.09 | 102.41 | -17.47%
Writing | 34.52 | 34.42 | -0.28%
Waiting | 16608.43 | 12558.83 | -24.38%
Verify | 39.45 | 56.87 | 44.17%
Total | 16806.48 | 12752.54 | -24.12%
Energy Usage | Static (uJ) | IODVS (uJ) | Delta
Idle | 157.07 | 138.95 | -11.54%
Writing | 26.48 | 26.23 | -0.93%
Waiting | 14021.97 | 10126.95 | -27.78%
Verify | 89.86 | 91.88 | 2.25%
Total | 14295.38 | 10384.02 | -27.36%

## Slide 18
SwissBit Micro-SD Card
Kingston Micro-SD Card
Energy Usage | Static (uJ) | IODVS (uJ) | Delta
Idle | 24.63 | 16.89 | -31.40%
Writing | 89.74 | 91.45 | 1.90%
Waiting | 122.44 | 97.39 | -20.46%
Verify | 54.00 | 57.53 | 6.53%
Total | 290.81 | 263.26 | -9.47%
Energy Usage | Static (uJ) | IODVS (uJ) | Delta
Idle | 66.25 | 43.53 | -34.30%
Writing | 25.01 | 25.72 | 2.85%
Waiting | 3726.20 | 2839.78 | -23.79%
Verify | 74.58 | 72.59 | -2.67%
Total | 3892.04 | 2981.62 | -23.39%

## Slide 19: Honeywell HIH6130 Temperature / Humidity Sensor
I2C devices operate in open-collector mode. The bus is pulled to the device Vdd.
Therefore, only reading a response from the device requires matched voltages
Has the added benefit that high voltages increase I2C speed
Energy Usage | Static (uJ) | IODVS (uJ) | Delta
Idle | 10.277369 | 6.2822829 | 61.13%
Command | 1.6786557 | 1.0474309 | 62.40%
Waiting | 399.0716 | 245.89278 | 61.62%
Reading | 4.3045919 | 4.4171913 | 102.62%
Total | 415.33221 | 257.63969 | 62.03%

## Slide 20: Observations
Device timing is specified with slack per the datasheet
The current profile of most devices indicates early completion
Can we identify early completions to further reduce energy consumption (and reduce latency)?
  Via: Time? – Energy? – Current?

## Slide 21: PRIME
Precise Real-time In-circuit Micro Energy management system
Faster MCU
More Memory
More Analog Channels
More Devices
More Bandwidth
Run-Time Configurability

## Slide 22: ASDM-300F Slide

## Slide 23: PPS-330D Slide

## Slide 24: PLR-5010D Slide

## Slide 25: STM32F429 Discovery Board
STM32F429 MCU @ 180MHz
  2MB FLASH, 512KB RAM
  3x simultaneously sampling ADCs
    2.2 MSPS @ 10-bit resolution
On board 64MB SDRAM
On board ST-Link in-circuit debugger
High-accuracy external oscillator
On board push buttons, LEDs and LCD with touch-screen
Access to every MCU pin via a 2x 100mil spaced dual row headers.

## Slide 26: Discovery Expansion Board
Hosts the STM32 Discovery Board
Provides all original PEGMA peripherals and
  NAND serial flash
  Optical Proximity Sensor
  Wi-Fi
  Bluetooth
  Programmable load regulators
Adds 2 more voltage domains
Peripheral Device Isolation
USB 2.0 Hi-Speed Communication

## Slide 27: PACER Peripheral Activity Completion Estimation and Recognition
Use the PRIME assembly to detect early completion of peripheral operations
  PACER-T
    Uses time-based heuristics
    Binary search of success or failure
  PACER-E
    Uses energy based heuristics
    Binary search of success or failure
    Original timing specifications maintained
  PACER-C
    Uses return-to-idle current profile
    Original timing specifications maintained

## Slide 28: EEPROM PACER-E Example

## Slide 29: Outline
Motivation / Problem Statement
  2 Slides
Related Work
  1 Slide
Methods
  2 Slides
Results
  6 Slides
Summary
  1 Slide
Future Work
  1 Slide
Questions / Further Discussion
  3 Slides

## Slide 30: Comparison
Requirements
Requires an adjustable regulator (SMPS realistically)
  Adds cost
  Potentially adds complexity
Requires some method of modulation
  PWM, DAC, Digital Pot., etc.
Requires specific knowledge of peripheral operation
  Second-Sourcing may be impacted
Voltage slack is decreased
Benefits
Significant energy savings throughout the dominant periods of operation
  May benefit cost
  May yield better performance
    RSM distance
    Thermal impact of relays
Near-zero CPU impact
Near-zero performance impact
Driver retrofit isn’t complex
Regulator modulation can be as simple or as complex as required

## Slide 31: Conclusions / Further Research
The application of IODVS is need-specific
  We have used a DAC here because it gives us the greatest flexibility, other solutions are far less complex and less costly
  You could just as easily use a MOSFET connected to the FB chain
  The best voltages to use need to be researched before design
    And with respect to EVERY device on the domain!
Further Research
  Write-completion predictor for polling based protocols (SD in particular)
  Cost model in terms of component reduction (NV-RAM electrolytic capacitor) vs component addition (SMPS modulation)
  SMPS response time / efficiency
Thank you!