## Slide 1: IODVS
Intra-Operation Dynamic Voltage Scaling

## Slide 2: Agenda
Who
What
Why
How
Results
Implications

## Slide 3: About Me
ADMMicro / Gridpoint
  Energy Management / Building Automation
  Sub-metering building loads (HVAC / Lighting / etc.)
  Environmental / Lighting Control
    Communicating thermostats / remote sensors
Elster
  Utility Metering (Gas / Water / Electricity)
    Measurement accuracy and data integrity are key!
    Communication via 900MHz Mesh / 2.4GHz Zigbee / 2G/3G
NCSU
  Working with Dr. Dean on low-power embedded systems
    Mitigating performance loss due to power requirements … or at least quantifying them

## Slide 4: Motivating Example: Remote Sensor Module
CAT5 Resistance: 29Ω / 1000ft
; Need 6V at load
Assume 4 devices @ 50mA
Assume 12Vdc output
Ω
RS485 max distance is rated for 4000ft over CAT5
Maximum distance is therefore limited by power consumption rather than line impedance
50mA per device is worst-case
  Can we decrease the worst case?

## Slide 5: Motivating Example: Logging Sensor

## Slide 6
Remote Sensor Module V2
Zone Sensor Module

## Slide 7: Motivating Example: Rex Electricity Meter
Maxim 8051 Metrology Core
  Uses EEPROM
    Energy Usage
    Demand Intervals
    Profile Information
    NV-RAM
TI Cortex-M3 Core
  Uses Serial flash
    Network routing data
    Encryption Keys?
  Radio Interface
Ember Zigbee
  Radio Interface

## Slide 8: NV-RAM Functionality
EEPROM has a limited write-cycle count (~1,000,000)
Serial flash is typically ~100,000
Some values need to be updated constantly and preserved across power failures
  Typically indexes into logs
  Energy accumulations
  Status information
Solution: Use RAM, and use an interrupt to back it up as power fail occurs
  Requires a capacitor capable of holding Vdd while backup is in progress
Actual communication is only 7.7% of the total write time. The other 92.3% is a mandatory wait period imposed by the chip ‘page-write time’
How can we decrease the energy consumed during the page write time?

## Slide 9: How: PEGMA
Peripheral Energy Generation Measurement and Allocation
4x + 1 input (boost) SMPS
3x output boost SMPS
8 independently adjustable buck SMPS domains
  MCU: STM32F205
    2x 10-bit DAC
    3x 12-bit ADC (2 MSPS per)
  Analog
  SRAM
  SPI Peripherals
    EEPROM
    Serial Flash
    Temp/Humidity Sensor
    Micro-SD Card
  Battery Charging
  Communications
  LEDs / Pushbuttons
  Relays
I/O Voltage and Current Measurement on each SMPS
  Allows us to measure efficiency!

## Slide 10: Adjustable SMPS
TPS62240 efficient at light loads
  ~80% at 1mA
I/O current measured by MAX4376
  “High Side” sense resistor is used, differential across is multiplied by the amplifier gain
  2MHz GBP, G = 20
Output Voltage modulated by current into the FB pin
  Therefore D9 allows the SMPS to enter a ‘default’ state
  And U25 / R105 allow FB current to be modulated by BUCKADJ3
  C144 holds the adjustment voltage so that other domains can be ‘refreshed’ in round robin fashion

## Slide 11: Peripheral Domain
Honeywell HIH6130 (I2C) Temperature/Humidity Sensor
  Vmax: 5.5V
  Vmin: 2.3V
Microchip 25AA512 EEPROM
  Vmax: 5.5V
  Vmin: 1.8V
Numonyx M25PX16 (16Mbit)
  Vmax: 3.6V
  Vmin: 2.3V
SPI Mode SD Cards
  Lexar SDSC: 1.0GB
  Sandisk: SDSC 1.0GB
  Swissbit: SDSC 512MB
  Kingston: SDSC 2.0GB
    Vmax: 3.6V
    Vmin: 2.7V (operating)
    Vmin: 2.0V (Idle/Read)

## Slide 12: Microchip 25AA512 EEPROM
Hu
State | Static (uJ) | IODVS (uJ) | Delta
Idle | 10.24 | 3.49 | -65.91%
Write | 13.79 | 17.85 | 29.47%
Wait | 64.59 | 33.71 | -47.80%
Verify | 17.58 | 17.40 | -1.02%
Idle | 8.81 | 7.96 | -9.57%
Total | 115.02 | 80.43 | -30.07%

## Slide 13: Numonyx 25PX16 Serial Flash
Hu
State | Static (uJ) | IODVS (uJ) | Delta
Idle | 10.73 | 5.63 | -47.58%
Read | 71.51 | 72.36 | 1.19%
Erase | 2.47 | 2.47 | -0.13%
Write* | 89.48 | 99.16 | 10.82%
Wait* | 574.84 | 365.75 | -36.37%
Verify | 83.78 | 52.77 | -37.02%
Idle | 38.92 | 38.20 | -1.85%
Total | 2666.18 | 1614.57 | -39.44%

## Slide 14: SD-Card Timing Variations
These tests tend to be non-deterministic