## Slide 1: PACER Peripheral Activity Completion Estimation and Recognition
Daniel Moore
January 23rd, 2018

## Slide 2: Motivating Example: Logging Sensor
Upon detecting a loss of power
MCU goes into sleep mode
Wakes up periodically
Samples external temperature sensors
Logs them to EEPROM
EEPROM dominates energy consumption
Decreases logging lifespan
Communicates via RS485
CAT5 Resistance: 29Ω / 1000ft
; Need 6V at load
Assume 4 devices @ 25mA
Assume 12Vdc output
Ω
RS485 is rated for 4000ft over CAT5
Distance limited by power consumption, not line impedance
25mA per device is worst-case
  Can we decrease the worst case and thereby increase battery life, increase maximum distance and potentially decrease cost?
Commercial / Industrial Temperature Logger
    Power Supply
    RS485 Communications
    Non-Volatile Storage (EEPROM)
    Micro-controller
    Analog Input

## Slide 3: Motivating Example: Electricity Meter
Metrology + Comms Processors
Uses EEPROM
  Energy Usage
  Demand Intervals
  Profile Information
  NV-RAM
Communications MCU
Uses Serial flash
  Network routing data
  Firmware Updates
  NV-RAM
Capacitor allows the system to run for a period of time after power fails
Some values need to be updated constantly and preserved across power failures
Typically indexes into logs
Energy accumulations
Status information
EEPROM has a limited write-cycle count (~1,000,000)
Serial flash is typically ~100,000
Solution: Use RAM, and interrupt to back it up as power fail occurs
Requires a capacitor capable of holding Vdd while backup is in progress
Storage capacity is best described as energy limited!
Actual communication is only 7.7% of the total write time. The other 92.3% is a mandatory wait period imposed by the chip ‘page-write time’
Residential / Commercial Electricity Meter
  Power Supply / Metering
  Metering MCU
  Metering EEPROM
  Communications MCU
  Communications Serial Flash

## Slide 4: IODVS Observations
Device timing is specified for the worst case per the data sheet. Timing slack exists.
The current profile of most devices indicates early completion
Can we identify early completions to further reduce energy consumption (and reduce latency)?
  Via: Time? – Energy? – Current?
  Need real-time actionable intelligence!

## Slide 5: PRIME
Precise Real-time In-circuit
Micro Energy management system
STM32F429 MCU @ 180MHz
  2MB FLASH, 512KB RAM
  3x simultaneously sampling ADCs
    2.2 MSPS @ 10-bit resolution
  Multi-channel DMA + MEM2MEM DMA
On board 64MB SDRAM
Why not just use interrupts Polling?
*Not universally supported
*Extra conductor
* Can’t perform IODVS

## Slide 6: ASDM-300F
TPS62240 efficient at light loads: ~80% at 1mA
Additional Micrel LDO “Ripple-Blocker” regulator for lower switching noise
  Lower than 20mvpp  Cannot measure via typical oscilloscope
Dual Channel Current Sense Amplifier MAX4377
  For simultaneous measurement of input and output current
SMPS and LDO feedback adjust simultaneously
8-Pin DIP Pinout compatible
I/O current measured by MAX4376
  “High Side” sense resistor is used, differential across is multiplied by the amplifier gain
  2MHz GBP, G = 20

## Slide 7: PPS-330D
Uses a 24 74HC139 decoder to switch the voltage domain supplied to an external peripheral
Ground can be disconnected entirely
8-Pin DIP pinout compatible

## Slide 8: Discovery Expansion Board
Hosts the STM32 Discovery Board
Provides all original PEGMA peripherals and
  Honeywell HIH6130 (I2C) Temperature/Humidity Sensor
  Microchip 25AA512 EEPROM
  Numonyx M25PX16 (16Mbit)
  SPI Mode SD Cards
    Lexar SDSC: 1.0GB
    Sandisk: SDSC 1.0GB
    Swissbit: SDSC 512MB
    Kingston: SDSC 2.0GB
  Optical Proximity Sensor
  Wi-Fi
  Bluetooth
  Programmable load regulators
Adds 2 more voltage domains
Peripheral Device Isolation
USB 2.0 Hi-Speed Communication

## Slide 9: PACER Peripheral Activity Completion Estimation and Recognition
Use PRIME to detect early completion of peripheral operations
3 Algorithms available:
  PACER-T: Time based heuristic
  PACER-E: Energy based heuristic
  PACER-C: Current based heuristic
Sub-Operations specified as a triplet:
  [T1, E1, C1]: Operation is considered complete when ANY of these conditions are satisfied
Operations specified as a set of up to 3 sub-operations:
  [[T1, E1, C1], [T2, E2, C2], [T3, E3, C3]]: Suitable for devices like serial flash
  Can diversify your metrics among sub-operations!
    Use time for sub-op1, energy for sub-op2, etc.

## Slide 10: EEPROM PACER-E

## Slide 11: EEPROM PACER-E + IODVS

## Slide 12: EEPROM Results
Energy (uJ) |  |  |  |  |  |  |  | 
State | Control | IODVS | PACER-T | PACER-T + IODVS | PACER-E | PACER-E + IODVS | PACER-C | PACER-C + IODVS
Idle | 6.03 | 2.47 | 6.04 | 2.52 | 6.06 | 2.47 | 6.13 | 2.48
Writing | 2.71 | 2.55 | 2.73 | 2.51 | 2.69 | 2.50 | 2.80 | 2.58
Waiting | 46.84 | 33.85 | 37.89 | 27.85 | 33.59 | 25.06 | 35.47 | 26.24
Read | 3.50 | 3.48 | 3.29 | 2.04 | 3.51 | 3.49 | 3.55 | 3.21
Idle | 5.89 | 5.76 | 15.30 | 13.42 | 14.97 | 14.16 | 14.50 | 14.03
Test Total | 53.05 | 39.88 | 43.91 | 32.40 | 39.79 | 31.06 | 41.82 | 32.03
Delta | 0.00% | -24.83% | -17.24% | -38.93% | -25.00% | -41.46% | -21.17% | -39.62%
Latency (ms) |  |  |  |  |  |  |  | 
State | Control | IODVS | PACER-T | PACER-T + IODVS | PACER-E | PACER-E + IODVS | PACER-C | PACER-C + IODVS
Idle | 1.025 | 1.025 | 1.026 | 1.025 | 1.026 | 1.025 | 1.038 | 1.038
Writing | 0.429 | 0.43 | 0.429 | 0.429 | 0.429 | 0.43 | 0.429 | 0.429
Waiting | 5.045 | 5.044 | 3.508 | 3.507 | 3.54 | 3.508 | 3.603 | 3.653
Read | 0.506 | 0.508 | 0.506 | 0.507 | 0.506 | 0.506 | 0.507 | 0.508
Idle | 0.994 | 0.992 | 2.53 | 2.531 | 2.498 | 2.53 | 2.422 | 2.371
Operation Total | 5.98 | 5.982 | 4.443 | 4.443 | 4.475 | 4.444 | 4.539 | 4.59
Delta | 0.00% | 0.03% | -25.70% | -25.70% | -25.17% | -25.69% | -24.10% | -23.24%
PACER algorithms reduced energy consumption by ~25%
  PACER-E appears to be the most effective on its own for this device
PACER + IODVS dramatically reduced energy consumption
  PACER algos are within the margin of error to each other for this case

## Slide 13: NOR Serial FLASH PACER-T

## Slide 14: NOR Serial FLASH PACER-T + IODVS

## Slide 15: NOR Serial Flash Results
Energy (mJ) |  |  |  |  |  |  |  | 
State | Control | IODVS | PACER-T | PACER-T + IODVS | PACER-E | PACER-E + IODVS | PACER-C | PACER-C + IODVS
Idle | 6.04 | 4.66 | 6.05 | 4.61 | 6.07 | 4.65 | 6.15 | 4.63
Reading | 49.99 | 50.08 | 58.08 | 50.21 | 50.13 | 49.89 | 49.87 | 50.14
Erase | 0.95 | 0.96 | 0.91 | 0.94 | 0.96 | 0.97 | 0.99 | 0.95
Total Write | 39.17 | 36.31 | 63.05 | 41.26 | 37.68 | 20.40 | 37.36 | 17.81
Total Wait | 2138.32 | 1713.89 | 1211.99 | 1029.52 | 1501.73 | 1178.32 | 1319.34 | 1040.74
Reading | 48.60 | 48.78 | 51.91 | 31.72 | 48.59 | 33.76 | 48.47 | 42.02
Idle | 37.05 | 33.13 | 929.24 | 711.59 | 689.63 | 576.83 | 859.97 | 657.46
Total No Idle | 2277.02 | 1854.68 | 1391.98 | 1158.26 | 1645.17 | 1287.98 | 1462.18 | 1156.28
Delta | 0.00% | -18.55% | -38.87% | -49.13% | -27.75% | -43.44% | -35.79% | -49.22%
Latency (ms) |  |  |  |  |  |  |  | 
State | Control | IODVS | PACER-T | PACER-T + IODVS | PACER-E | PACER-E + IODVS | PACER-C | PACER-C + IODVS
Idle | 1.04 | 1.04 | 1.04 | 1.04 | 1.04 | 1.04 | 1.05 | 1.05
Reading | 4.27 | 4.27 | 4.27 | 4.27 | 4.27 | 4.27 | 4.27 | 4.27
Erase | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08
Total Write | 3.31 | 3.32 | 3.31 | 3.32 | 3.31 | 3.32 | 3.31 | 3.32
Total Wait | 231.57 | 231.57 | 69.47 | 66.92 | 104.81 | 120.17 | 80.15 | 79.06
Reading | 4.64 | 4.64 | 4.27 | 4.63 | 4.64 | 4.73 | 4.64 | 4.64
Idle | 7.09 | 7.08 | 169.55 | 171.74 | 133.86 | 118.38 | 158.50 | 159.57
Total No Idle | 243.87 | 244.92 | 82.45 | 80.26 | 118.14 | 133.62 | 93.50 | 92.43
Delta | 0.00% | 0.43% | -66.19% | -67.09% | -51.55% | -45.21% | -61.66% | -62.10%
PACER algorithms reduced energy consumption by ~33%
  PACER-T appears to be the most effective on its own for this device
PACER + IODVS dramatically reduced energy consumption + latency
  PACER-T + IODVS Reduced latency by 67%, and energy by 49%

## Slide 16: NAND Serial FLASH PACER-T

## Slide 17: NAND Serial FLASH PACER-T + IODVS

## Slide 18: NAND Serial Flash Results
Latency (ms) |  |  |  |  |  |  |  | 
State | Control | IODVS | PACER-T | PACER-T + IODVS | PACER-E | PACER-E + IODVS | PACER-C | PACER-C + IODVS
Idle | 1.04 | 1.04 | 1.04 | 1.04 | 1.04 | 1.04 | 1.05 | 1.05
Reading | 5.00 | 5.00 | 5.00 | 5.00 | 5.00 | 5.00 | 5.00 | 5.00
Erase | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08
Total Write | 3.31 | 3.32 | 3.31 | 3.31 | 3.31 | 3.32 | 3.31 | 3.31
Total Wait | 57.61 | 57.62 | 19.26 | 19.27 | 25.92 | 25.92 | 36.19 | 36.20
Reading | 5.28 | 5.28 | 5.29 | 5.29 | 5.28 | 5.28 | 5.28 | 5.29
Idle | 9.68 | 9.67 | 48.02 | 48.01 | 41.37 | 41.36 | 31.09 | 31.07
Active Total | 71.28 | 71.29 | 32.94 | 32.95 | 39.59 | 39.60 | 49.86 | 49.87
Delta | 0.00% | 0.01% | -53.79% | -53.78% | -44.46% | -44.45% | -30.05% | -30.03%
Energy (mJ) |  |  |  |  |  |  |  | 
State | Control | IODVS | PACER-T | PACER-T + IODVS | PACER-E | PACER-E + IODVS | PACER-C | PACER-C + IODVS
Idle | 5.62 | 4.12 | 5.54 | 4.07 | 5.58 | 4.08 | 5.64 | 4.14
Reading | 71.49 | 71.57 | 72.58 | 71.52 | 71.45 | 72.10 | 71.54 | 71.39
Erase | 1.58 | 1.59 | 1.53 | 1.58 | 1.55 | 1.49 | 1.55 | 1.52
Total Write | 51.88 | 48.14 | 75.40 | 70.70 | 73.01 | 70.19 | 51.63 | 44.66
Total Wait | 1052.98 | 806.15 | 802.63 | 584.87 | 817.59 | 596.84 | 887.28 | 670.32
Reading | 69.97 | 69.81 | 73.11 | 73.27 | 72.90 | 73.11 | 72.75 | 72.85
Idle | 52.31 | 44.66 | 249.37 | 187.25 | 234.28 | 158.54 | 149.37 | 133.95
Active Total | 1247.90 | 997.26 | 1025.25 | 801.95 | 1036.50 | 813.72 | 1084.76 | 860.73
Delta | 0.00% | -20.08% | -17.84% | -35.74% | -16.94% | -34.79% | -13.07% | -31.03%
PACER algorithms reduced energy consumption by ~15%
  PACER-T appears to be the most effective on its own for this device
PACER + IODVS dramatically reduced energy consumption + latency
  PACER-T + IODVS Reduced latency by 54%, and energy by 36%

## Slide 19: HIH-6130 Environment Sensor PACER-T

## Slide 20: HIH-6130 Environment Sensor PACER-T + IODVS

## Slide 21: HIH-6130 Results
PACER algorithms reduced energy consumption by ~25%
  PACER-T appears to be the most effective on its own for this device
PACER + IODVS dramatically reduced energy consumption + latency
  PACER-T + IODVS Reduced latency by 54%, and energy by 36%
Energy (mJ) |  |  |  |  |  |  |  | 
State | Control | IODVS | PACER-T | PACER-T + IODVS | PACER-E | PACER-E + IODVS | PACER-C | PACER-C + IODVS
Idle | 5.19 | 3.60 | 5.28 | 3.64 | 5.24 | 3.62 | 5.33 | 3.67
Writing | 1.75 | 0.98 | 1.76 | 0.93 | 1.73 | 0.98 | 1.76 | 1.00
Waiting | 325.95 | 231.17 | 254.14 | 120.39 | 240.29 | 169.62 | 223.65 | 159.00
Idle | 0.08 | 0.05 | 0.09 | 0.05 | 0.12 | 0.10 | 0.09 | 0.05
Reading | 2.80 | 2.64 | 2.98 | 3.10 | 3.37 | 3.30 | 2.95 | 2.92
Idle | 28.04 | 26.18 | 105.49 | 83.50 | 106.34 | 84.62 | 105.31 | 83.60
Active Total | 330.50 | 234.79 | 258.88 | 124.41 | 245.39 | 173.89 | 228.36 | 162.91
% Decrease | 0.00% | 28.96% | 21.67% | 62.36% | 25.75% | 47.39% | 30.91% | 50.71%
Latency (ms) |  |  |  |  |  |  |  | 
State | Control | IODVS | PACER-T | PACER-T + IODVS | PACER-E | PACER-E + IODVS | PACER-C | PACER-C + IODVS
Idle | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 1.03 | 1.03
Writing | 0.23 | 0.44 | 0.23 | 0.44 | 0.23 | 0.44 | 0.23 | 0.44
Waiting | 45.27 | 45.27 | 31.66 | 31.44 | 31.45 | 31.41 | 31.70 | 31.60
Idle | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Reading | 0.49 | 0.95 | 0.49 | 0.95 | 0.49 | 0.95 | 0.49 | 0.95
Idle | 4.98 | 4.32 | 18.59 | 18.15 | 18.80 | 18.18 | 18.54 | 17.98
Active Total | 45.99 | 46.65 | 32.38 | 32.82 | 32.17 | 32.80 | 32.42 | 32.98
% Decrease | 0.00% | -1.44% | 29.59% | 28.63% | 30.05% | 28.69% | 29.50% | 28.28%

## Slide 22: microSD Cards…
Recall the current profile of the Swissbit microSD Card
  2048 averaged samples indicate completions at a wide variety of times!
Indicates onboard caching. We’ll prove it on each device.
Only PACER-C logically makes sense to detect these completions

## Slide 23: Caching Example
Typical IODVS write (cache miss)
PACER-C write
cache hit detected

## Slide 24: Sandisk Caching Example
Typical IODVS write (cache miss)
PACER-C write
cache hit detected
Note the current multiple

## Slide 25: Sandisk microSD Results
PACER-C improvement realizes the energy benefit of cache-hits

## Slide 26: Lexar microSD Results

## Slide 27: Swissbit microSD Results
PACER-C improvement realizes the energy benefit of HIGHLY variable response times

## Slide 28: Kingston microSD Results
PACER-C improvement limited by highly clustered response times, extremely fast operation times, low wait-energy penalty. Still, slightly faster response time

## Slide 29: PACER Results / Analysis
Significant energy / latency savings on its own merit
Enhanced further by IODVS and provides completion detection
PACER-T and PACER-C are most effective for the devices tested
PACER-T requires no extra circuitry whatsoever
PACER-E requires analog feedback but is computationally friendly
  DMA + MAC units are currently very common on MCU
PACER-C can provide the best performance for highly non-deterministic response times.
  May be MCU friendly if specialized ADC HW is available – there currently exists interrupt-on-threshold MCU hardware